Just received my new rig, neither the supplier nor Kenwood had the mods available to date.

- Remove the bottom cover, 5 screws (not the speaker side).

- Locate and remove "W601" (chip resistor) and "W602" (green wire). They are located within 2 inches of the optional VS-3 voice synthesizer board.

- Reassemble radio and after power-up, press the reset switch on the front of radio.

Here is your new TRANSMIT range

136.000	- 174.995

400.000	- 469.995

This is the RECEIVE range (mode selected).

118.000	-  135.995

136.000	-  199.995

200.000	-  299.995

300.000	-  399.995

400.000	-  523.995

800.000	-  823.990

849.000	-  869.990

894.000	-  913.990

934.000	- 1299.990