Technical Information (Ref No. : ZSL00006 / date : November 28, 2005)

Following information is regarding the modification of expanding the TX frequency coverage of the IC-7000

- Remove the 8 screws from the upper cover (not the screws of the loudspeaker)

- Remove the 2 screws of the module (down left and up right) and remove the module

- The diode-matrix is visible with D2168, D2169, D2170 en D2172 in place

- Remove all diodes (3) except D2170

|  | D2168 | D2169 | D2170 | D2171 | D2172 |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | NO | NO | NO | NO | NO | 1.6 - 25.999999 MHz 28.0 - 29.999999 MHz 50.0 - 54.000000 MHz 144.0 - 146.000000 MHz 430.0 - 440.000000 MHz |
| 2 | NO | YES | NO | NO | NO | 1.6 - 54.000000 MHz 118.0 - 174.00000 MHz 400.0 - 470.000000 MHz |
| 3 | NO | NO | YES | NO | NO | 0.1 - 199.999999 MHz 400.0 - 470.000000 MHz |
| ****************Initial Diode Matrix geleverd in Europa******************* Diode Matrix Condition on the MAIN UNIT |
|  | D2168 | D2169 | D2170 | D2171 | D2172 |  |
|  | YES | YES | YES | NO | YES |  |